VILLAGE OF WELLSBURG BUILDING DEPARTMENT 295A Main St, Wellsburg, NY 14894 PERMIT APPLICATION 607 271 9129, / Fax: 607 271 9182 All applicable sections of this application must be completed - incomplete applications will not be considered. Type of permit requested: ( ) Building ( ) Zoning ( ) Demolition ( ) Excavation/Fill

Property Owner: Date: Project Address: Day Time Phone: Tax Map Number: Zoned: Subdivision Name: For certification of proposed use and occupancy for construction, Village of Wellsburg, County of Chemung; Undersigned petitions permission for (check all that apply): ( ) New building ( ) Deck / Porch ( ) Swimming pool ( ) Electrical ( ) Fence ( ) Change of use ( ) Repair ( ) Addition ( ) Heating equip. ( ) Pole barn / Shed ( ) Plumbing ( ) Sign ( ) Renovations ( )

Description of the proposed project and its proposed use:

Type of use: ( ) Residential ( ) Commercial ( ) Industrial ( ) Other: Construction type: ( ) Wood ( ) Steel ( ) Masonry ( ) Other: Project dimensions: Width: Length: Height: Sq. footage: Set backs from lot lines: Front: Rear: Side 1: Side 2: Lot frontage: Lot depth: Estimated value of all work, materials and labor: $ Is the project (circle one): In a flood hazard zone? Yes No Within 100’of any wetlands or open water? Yes No

Contractor: Contact person: Address: Phone: If the construction or alteration will have an effect on either structural or public safety or exceed $20,000 in cost, all plans submitted must bear the original seal and signature of a NYS licensed Professional Engineer or Registered Architect. (NYS Education Law sections 720 9 & 7303) Architect: RA PE Lic. No: Address: Phone:

APPLICANT CERTIFICATION: I hereby certify that I have read the instructions and examined this completed application and know the same to be true and correct. All work done under this permit will meet the requirements of the New York State Uniform Fire Prevention and Building Code and all ordinances and regulations of the Village of Wellsburg. I also understand that the granting of this permit does not presume to give authority to violate or cancel the provisions of any other state or local law regulating construction or land use or the performance of construction. INSPECTIONS REQUIRED: I understand that I am respons ible to ensure that the inspections listed on the reverse side of this application are performed as construction progresses and that in no case shall construction proceed beyond any required inspection until approved by the Code Enforcement Officer. I understand that failing to have a required inspection performed would constitute a violation punishable by a fine not to exceed $1,000 per day and imprisonment not to exceed one year. CONSENT TO ENTER PROPERTY: I recognize that by signing this application, I am giving consent to employees of the Village of Wellsburg to enter the subject property for the purpose of obtaining information relevant to the processing of this application. I also understand that by acceptance of a Permit, I agree to allow representatives of the Village of Wellsburg access to the properties covered by the Permit, at reasonable times, for the purpose of ascertaining compliance with the Permit. SIGNATURE OF OWNER O F PREMISES: DATE:

Official Use Only

Date Completed: Application No.: FM V: Fee:

Date Approved: Date Notified: Approved By:

Date Denied: Date Notified: Denied By: Reason Denied:

INSPECTION SCHEDULE FOR NEW CONSTRUCTION

All applicable inspections listed below are MANDATORY.

1)    FOOTINGS / POSTS :	Typical Foundation Cross-section

To be placed on undisturbed soil, a minimum of 42”

deep, formed on both sides of the concrete with	Sill Plate	Sill Insulation

2 by X lumber, sized in accordance with the NYS	(Pressure Treated)

Uniform Building Code.  Forms  are to be squared	Anchor Bolts	R-11 Insulation and leveled to fit the structure.  Rebar is to be	Grade	from the sill to

| installed per ACI specs, each bar to be aligned |  | 48” below grade |
| --- | --- | --- |
| under edges of foundation. Rebar is to be located | (Exterior Side) | (Interior, exterior |
| one-third up in the forms and is to be supported | Waterproofing | or combination) |

on chairs or wire -tied to the forms, overlaps to be	and

a minimum of 24” and tied on both ends.	Insulation	Foundation Wall

CALL FOR INSPECTION BEFORE ORDERING

CONCRETE OR FILLING POST HOLES!	Filter	Floor

Perimeter drainage is to be installed as shown in the	Paper drawing to the right.  If there is a problem with water

or mud there are alternatives, please call.  If a sump	Gravel or		Rebar – (Aligned pump is used; a similar drainage system is required	Crushed Stone	Footer Drain	  with wall edges)

on the inside.  If a walk-out basement is anticipated, the

foundation in that area must be below the frost line and insulated.

COPIES OF ALL CONCRETE LOAD TICKETS THAT CERTIFY THE COMPRESSIVE STRENGTH OF CONCRETE MUST BE SUBMITTED TO THE CODES OFFICE.

2)    FOUNDATION :  Foundation wall including sill plate, anchor bolts (10” in length, 6’ on center and 12 inches from the end of any section of sill plate), waterproofing, drainage tile and exterior insulation BEFORE BACKFILLING.

3)    FRAMING:  Vertical and horizontal members, sub-flooring and wall and roof sheathing.  Interior members after electrical and plumbing rough-ins and BEFORE INSULATING OR EN CLOSING.

4)    MECHANICALS, CHIMNEYS & FIREPLACES :  To be inspected BEFORE ENCLOSING.

Must be approved before insulation or gypsum is applied.  All heating devices are to comply with Manufacturer’s specs.

5)    ELECTRICAL:  Rough-in electrical inspection is  required PRIOR TO INSULATION OR DRYWALL.

We need to see the inspection approval from the following, applicable agency before insulation is started: Approved Electrical Inspection Agencies:  NY BOARD OF FIRE UNDERWRITERS.

6)    PLUMBING:  Rough-in plumbing inspection is required PRIOR TO INSULATION OR DRYWALL.  We need to see the inspection approval from the CHEMUNG COUNTY HEALTH DEPARTMENT before insulation is started.

7)    FIRE-STOPPING:  Vertical and horizontal firestopping after mechanical, electrical and plumbing rough-ins.

8)    INSULATION:  Batting insulation must be inspected PRIOR TO INSTALLING GYPSUM.  If insulation is blown

into attic or wall areas, vender certification is required.  INSULATION OF BASEMENT:  Joist cavities downward to

48” b elow grade are to be insulated with minimum R -11; inside or outside.  Fire -rated material covering is required inside.

9)    FIRE SEPARATION:  Fire separations for attached garages are to be as follows:

5/8” type X gypsum wallboard on garage side of the partition between the garage and the house and 5/8” or ½” type X gypsum on the house side . Complete coverage to underside of roof deck or entire garage ceiling coverage is required. Fasteners are to be 12 inches on center along framing members and counters sunk 1/32”. Where a room exists above the garage all load bearing garage walls are to be covered with 5/8” type X gypsum wallboard and the fasteners on the ceiling are to be 6 inches on center.  WALLBOARD MUST BE INSPECTED BEFORE FASTNERS ARE CONCEALED.

10)  FINAL BUILDING INSPECTION:   Must be performed prior to occupancy or use.*

FINAL ELECTRICAL & PLUMBING INSPECTIONS :  Should be scheduled prior to final building inspection.

CERTIFICATE OF OCCUPANCY:  Must be obtained BEFORE OCCUPANCY OR USE TAKES PLA CE.

AS-BUILT SURVEY:  An as -built survey (structure location plotted on final survey by a N. Y. S. licensed surveyor) is required for all new homes and projects involving variances and may be required for other projects .

** CALL AT LEAST TWO DAYS AHEAD TO SCHEDULE INSPECTIONS **

(This is a general inspection schedule and may not include all of the required inspections that pertain to your individual project.)

*If the applicable certificate is not obtained prior to occupancy or use, legal action will be taken as outlined in the Village of Wellsburg

Zoning Ordinance.  Failure to have a required inspection certified by the Code Enforcement Officer will negate the issuance of a certificate.

FAILURE TO COMPLY WITH THIS INSPECTION SCHEDULE CAN RESULT IN THE ISSUANCE OF A STOP WORK ORDER, FINES NOT TO EXCEED $1,000 AND IMPRISONMENT NOT TO EXCEED ONE YEAR.

Village of Wellsburg

Code Enforcement Office

295A Main St

Wellsburg NY  14894

607 271 9129

BUILDING PERMIT APPLICATION PROCEDURE

A)	Complete all applicable sections of the Building Permit Application.  Incomplete applications will be returned.

B)	Sign and date the bottom of the application.

C)	Submit the following items with your completed application:

(Some may not apply to your project)

	Copy of deed or other proof of ownership or control of property.

	Copy of survey or plot plan indicating project location with dimensions and setbacks.

	Sewer connection approval.

	Building plans (Stamped by licensed NYS architect if over $20,000 or 1,500 square feet.)

	Energy Code certification.

	Truss design sheets or certificates.

	Electrical inspection application from NY Board of Fire Underwriters (463-8552).

	Liability insurance certificate.

- Workman’s compensation insurance certificate (c105.2, c105.21 or BP-1) or

- Owner exemption form (ask clerk for copy if doing yourself)

C)  The Code Enforcement Officer will normally review a completed application and approve

or deny within five days of receipt.

D)  All applicable inspections listed on the reverse side of the building permit application are    mandatory.  Please call five days ahead to schedule inspections.

E)  If you have any questions or need assistance with your application, please contact the

Village Clerk or Code Enforcement Officer at 271 9129 or 733 4044.